## Slide 1: Electronics for physicists
Lecture 4
Operational Amplifier

## Slide 2: Introduction
OPVs are many transistors at once
OPVs are good and cheap
Disadvantage: too bulky for systems with many read-out channels

## Slide 3: What are ap amps good for?
Universal flexible amplifies of voltages and currents
Charge-sensitive amplifiers
Buffer
Comparator
Active filters
Components in ADCs and DACs
…

## Slide 4: Operational amplifier (op-amp)
High-gain differential amplifier block
Differential input, single-ended output (usually)
Differential input is flexible and helps suppress noise sources
"+" non-inverting input;
"-" inverting input
AD: gain, best large e.g. 100 000

## Slide 5: Operational amplifier (op-amp)
Op-amp gain AD should be large and constant
Alas, this is not always so. Gain depends on input voltage, frequency and temperature …
Gain as a function of input voltage and of frequency
Saturation
Linear range
Low-pass behavior
(dominant pole)

## Slide 6: Op-amp as black box
Input resistance RG is very high, minimum MΩ to GΩ
Output impedance RA is low (voltage source)
Simplified op-amp circuit diagram. Supply voltage is not shown.

## Slide 7: Operational amplifier ICL7621
ICL7621 (Intersil) schematic
1012 Ω input impedance, 200 µW power, ±1V to ±8 V supply voltage, 75 db voltage gain, 2 µs rise time, 0.48 µs GBP, low-noise

## Slide 8: Positive and negative feedback
Feedback:
Some fraction of the output voltage is fed back to the op-amp input
Feedback can be positive (to non-inverting input) or negative (to inverting input)
We will mostly consider negative feedback below.
Schmitt trigger
Inverting amplifier

## Slide 9: Schmitt trigger
Positive feedback increases U+ for positive input voltage
Uaus is driven to equal Umax  trigger function
Output signal is essentially binary with two states:
Umax ≈ + UCC , Umin ≈ - UCC
+ Ucc
- Ucc
U-

## Slide 10: How to switch states?
Assume Uaus = Umax
Need U+ ≤ 0 to change output polarity
With and

changes output voltage to Umin

## Slide 11: Schmitt trigger hysteresis
Need strong input signal to overcome positive feedback  hysteresis.
Schmitt trigger symbol
or

## Slide 12: Inverting amplifier
Inverting amplifier
voltage
time
slow op-amp
Fast op-amp
Input signal
Fast op-amp shows overshoot and some ringing
Slow op-amp is fine but slow

## Slide 13: Golden rules
To analyse circuits with negative feedback we assume:
U+ = U- Note: U- differs from Uin due to feedback!
The op-amp input impedance is infinite. (No current flows into op-amp.)
The op-amp output impedance is small. (Output voltage does not depend
on load and output current.)
For the inverting amplifier, this results in:
(virtual ground)
I1
I2

## Slide 14: Non-inverting amplifier
Input voltage is applied to non-inverting mode
With golden rules:
Thus

## Slide 15: Voltage buffer
This circuit is a non-inverting amplifier with R1 =  and R2 = 0.
≈
What is the point of this circuit?
Output can provide larger current than unbuffered input.

## Slide 16: Operational amplifier as a control loop
and

Assuming op-amp output settles into a stable state, we can easily calculated gain…
For simplicity, we set KF = 1.
and

## Slide 17: Definitions
AD: open-loop gain
Leerlaufverstärkung
A: closed-loop gain
Verstärkung mit Rückkopplung
KR AD: loop gain
Schleifenverstärkung
Examples:
AD: 100 K
KR : R1/(R2 + R1) = 1/11, A ≈ 10
KR AD: 104

## Slide 18: Charge-integrating amplifier (CIA or CSA)
Integrator
Passive low-pass

What is the difference between “active” and “passive” integrators?
C is being charged up. Output voltage is going down!

## Slide 19: Differentiator
With golden rules:
The „active“ differentiator is much superior to passive CR differentiator. Why?

## Slide 20: High-pass
For or
small R this reduces to

## Slide 21: Logarithmic amplifier
With and
 and

## Slide 22: Exponential amplifier
Here the diode and resistor positions are swapped.

## Slide 23: Analog / Electronic (Transistor / IC)
In the 50s and 60s (even 70’s) electronic versions of the analog computer were available
Generally consisted of Op Amps with the ability to connect them to add, subtract, multiply integrate, etc.

## Slide 24: Real op-amps
Parameters of real and ideal op-amps. Values without feedback.
Ratio AD/AG should best be very large

## Slide 25: Equivalent circuit of inverting amplifier
U- = U1 corresponds to the voltage on the inverting input
Apply superposition principle. Assume Iaus = 0 and RG >> RD

## Slide 26: Equivalent circuit of inverting amplifier
U- is approx. 0 V (virtual mass)

## Slide 27: Op-amp gain frequency response
Most op amps are tailored to look like first-order
low-pass (dominant pole):
How does negative feed-back influence the frequency response?
If f << fg : (indep. of frequency!)
If f >> fg : and
1,000
1,000

## Slide 28: Gain vs. bandwidth
f0 = frequency at gain 1 (= 0 db)
One can trade off bandwidth and gain.
Reducing the amplification by a factor ten increases bandwidth by ten.
1,000
1,000
Gain-bandwidth-product (GBP)

## Slide 29: Oscillators
Square wave generator
There are two stable output voltage states:

## Slide 30
A stable oscillation requires a combined op-amp and feed-back phase shift of ± 360°
What is the phase shift of the three low-passes?
Phase shift oscillator

## Slide 31: Bode plot of first-order low-pass

## Slide 32: Many low-passes…
Maximum phase shift increases to n times -90°
Steepest slope at ω-3db
From: „Op amps for everyone“

## Slide 33
No external input
If phase shift of feed-back signal is ±360°, circuit may oscillate.
Resonance frequency depends on RC (here oscillation at ω = 1.73/RC)
Phase shift oscillator
Uaus
Uein
φ = -180°
φ = -60°
φ = -60°
φ = -60°

## Slide 34: Another phase shift oscillator
Chain of active integrator (op-amp), two low-pass filters and voltage buffer (op-amp).
Adjustable resistor acts as feed-back between op-amp 2 output and op-amp 1 input.
No external input! (Op-amp power supplies are not shown.)

## Slide 35: Oscillation condition
Assume stable oscillation with frequency ω and period T:
Let´s calculate U2 from U1 , U3 from U2 ,etc:

## Slide 36: Oscillation condition
Questions: Why 2 low-pass filters, rather than 1?
What is the output voltage?
Imaginary part = 0 
Real part = 1 
Thus

## Slide 37: Oscillator explained
Distinguish three scenarios …
Loop gain ADKR >> 1: Strong feed-back and limited amplification  stable output, no oscillation, A ≈ 1/KR => Good!
Loop gain << 1: Weak feed-back, very strong amplification, output tends to saturate A ≈ AD. => Not ideal for amplifier, but good for comparator.
If |ADKR| ≈ 1, we have to watch the sign of ADKR. For ADKR ≈ +1, see 2. For ADKR ≈ -1: => Oscillating condition (Barkhausen criterion)!
  For one negative feed-back turns into positive feed-back. Also the value of AD saturates, the effective feed-back is reduced. This is the oscillation condition.

## Slide 38: From amplifier to oscillator
Why is ADKR ≈ -1 bad for amplifiers?
For one negative feed-back turns into positive feed-back.
Also the value of AD saturates, and the effective feed-back is reduced.
Consider Uein to be small. Then KRAD = -1 implies:
Uaus (T) = - KR AD Uaus (t=0) = + Uaus(t = 0)
Uaus (t = 0) = Uaus (T) is compatible with oscillation.

## Slide 39: Phase margin
AD KR ≈ -1: => oscillating condition,
Barkhausen criterion!
Phase margin 90°
Rule of thumb: need of phase margin for stability
|AD| =

## Slide 40: AC-DC converter

## Slide 42
A more abstract view of feed-back

## Slide 43: Inverting Op-amp
Current-to-voltage converter
Shunt-shunt feed-back
Feed-back reduces input impedance
Feed-back reduces output impedance
A =
dVout
dIin
_____

## Slide 44
Non-inverting Op-amp
Series-shunt feed-back
Feed-back increases input impedance
Feed-back reduces output impedance
A =
dVout
dVin
____

## Slide 45
Feed-back makes for 4 op-amp types

## Slide 46: Negative impedance
Resistances R are positive and U = RI
With active circuit elements, negative impedances can be constructed! How?
Positive and negative feedback!

## Slide 47: Negative impedance converter (NIC)
Negative current  negative resistance

## Slide 48: Gyrator
Definition:
Circuit:

## Slide 49: Gyrator
with


## Slide 50: Amplifiers vs. oscillators
Feed-back yields closed-loop gain of
If , amplifier is stable and
If , amplifier oscillates (Barkhausen criterion)
Thinking in phase and amplitude, Barkhausen implies:
  a net phase shift of 180° (through passive filter network)
  a loop gain of 1
For stable frequency need well-defined oscillation condition and thus large dφ/d
=
=

## Slide 51: Wien bridge oscillator
Circuit elements:
1 op-amp
2 capacitors
4 resistors
1 R-diodes circuit
Wien bridge oscillator produces sinusoidal oscillation at a given frequency.

## Slide 52: Circuits elements
Negative feed-back loop through R10 + R11 + R12 defines gain
R12 and diodes make sure gain at start-up is larger than later
Positive feed-back is constrained by band pass. At resonance frequency, phase shift is 0° and band-pass output maximum
1 +
vs.
1 +
U+ = Uout

## Slide 53
Appendix

## Slide 54: Charge integrating amplifier
Integrator
Consider a current signal at the input of the op-amp
The current is converted into a voltage with gain dUout/dIin = 1/CF
To be considered:
noise and equivalent noise charge (ENC)
Ci / CD
discharge of feedback capacitor
1/CF = gain; A high
detector system with complete circuit including diode in reverse direction, filter, op-amp, etc.